## Slide 1: Saturated soil modelling: Griffith University: February 2010
Cam clay improved: nonlinearity and structure
David Muir Wood
d.muirwood@dundee.ac.uk

## Slide 2
Designer models: addition of extra features
Kinematic yielding
2. Cam clay
3. Mohr-Coulomb

## Slide 3
shear stress
mean stress
elastic - stiff
plastic – less stiff
shear stress
shear strain
classical elastic-plastic modelling of soil
for example, Cam clay (1963, 1968)

## Slide 4
stress
yield?
strain
typical actual response
void ratio
vertical stress
(log scale)
preconsolidation pressure
classical identification of yield from stress:strain response
geometrical construction for estimation of preconsolidation pressure

## Slide 5
Cam clay providing inspiration:
search for ‘Cam clay like’ yield loci
eg kaolin (Al-Tabbaa, 1984)

## Slide 6: yield loci for natural clays
collected by Graham et al (1988)

## Slide 7: typical experimental observation: stiffness falls steadily with monotonic straining: is there an elastic region?
shear stiffness degradation data for Quiou sand from resonant column and torsional shear tests (after LoPresti et al, 1997)
limit of elastic response??

## Slide 8: how do we objectively identify yielding? occurrence of irrecoverable strain? dissipation of energy in loading/unloading cycles? change in slope of stress:strain response?
stress
strain
a.
stress
strain
b.

## Slide 9
yielding of Bothkennar clay:
boundaries deduced from inspection of stress:strain response
Y1 approximately centred on in situ stress state
Y3 reflects natural structure – damaged by any irrecoverable strain - evanescent
after Smith et al (1992)

## Slide 10: kaolin revisited: isotropic consolidation histories
data from Al-Tabbaa (1987)

## Slide 11: kaolin revisited: one-dimensional consolidation histories
data from Al-Tabbaa (1987)

## Slide 12
q kPa
q kPa
q kPa
q kPa
p' kPa
p' kPa
p' kPa
p' kPa
plastic strain increments: approximate normality to kinematic yield loci
kaolin: Al-Tabbaa, 1987

## Slide 13: Deviatoric stress response envelopes
distortional stress probe rosettes
constant mean stress
cross anisotropy?
Ev > Eh
εd = 0.05, 0.2, 0.4, 0.6, 0.8, 1, 1.2%
σx
σy
σz
σx
σy
σz
A: isotropic compression
Hostun sand
Sadek, 2006

## Slide 14
distortional probing
constant mean stress
non-monotonic stress paths
stress probe rosettes
ABC … probe
AB … probe
σz
σx
σx
σy
σy
σz
Sadek, 2006

## Slide 15
distortional strain
0.05%: history recalled
1%: history ‘forgotten’
radial shearing AB
two corners ABC
Stress response envelopes: Hostun sand: small-medium strain
εd = 0.05, 0.2, 0.4, 0.6, 0.8, 1, 1.2%
Sadek, 2006

## Slide 16
comparison of 0.05% strain response envelopes for histories A, AB, ABC
stress response envelopes
small/medium strain stiffness
kinematic hardening
centre as indicator of current fabric
but strain too large
Sadek, 2006

## Slide 17
Designer models: addition of extra features
Kinematic yielding
2. Cam clay
3. Mohr-Coulomb

## Slide 18
Cam clay
elastic-hardening plastic model
volumetric hardening
associated flow – normality

## Slide 19
Cam clay
response in drained triaxial compression tests with constant p'
asymptotic approach to critical state
effect of overconsolidation ratio
sharp division between elastic and plastic response

## Slide 20
compare response of soil on nonmonotonic loading
with capability of single yield surface model
extension to simple models using kinematic hardening
and bounding surface plasticity

## Slide 21
compare response of soil on nonmonotonic loading with capability of single yield surface model
elastic-hardening plastic model expects elastic behaviour on reversal, sudden drop in stiffness at yield
soils typically show hysteretic behaviour on unload-reload cycles, steady change in incremental stiffness

## Slide 22
kinematic hardening extension
yield locus carried around with stress state – 'bubble' – strongly influenced by recent history
stiffness falls as yield 'bubble' approaches bounding surface – controlled by distance b
when loading with 'bubble' in contact with bounding surface model is identical to Cam clay

## Slide 23
assume relative size R of 'bubble'
assume rule for translation of 'bubble'
assume interpolation rule linking plastic stiffness with b
…otherwise identical to Cam clay

## Slide 24
kaolin
constant p' cycles
hysteresis
build up of volumetric strain
experiment
simulation
volumetric strain
distortional strain
η
η
η
η

## Slide 25
migration of 'bubble' during constant p' unloading after one-dimensional normal compression
hardening of 'bubble' and bounding surface
q kPa
p' kPa

## Slide 26
experiment
simulation
constant q cycles after one-dimensional normal compression

## Slide 27
add further effects in a similarly hierarchical way
cementation and structure: extension to 'bubble' model
natural soils often contain structure: bonding between particles: destroyed with mechanical or chemical damage

## Slide 28
design model in which yield surface has increased size as a result of the bonding
with plastic straining (or chemical weathering) the yield surface gradually shrinks to the yield surface, for remoulded, structureless material
extension of 'bubble' kinematic extension of Cam clay
all features of 'bubble' model retained
ratio of sizes of structure surface and reference surface gives indication of current degree of structure

## Slide 29
add measure of structure or bonding: single scalar parameter r
'bounding' surface now called 'structure' surface: size r times larger than a reference surface
structure lost whenever plastic strains occur
damage law:
damage plastic strain increment δεdp combines plastic volumetric and plastic distortional strain increments:
– additional parameter to control their relative importance
structure progressively disappears:
r  1 as plastic deformation increases

## Slide 30
logical: structureless soil is one which has been so mechanically pummelled that it has no remaining bonds between particles
particular forms of laboratory testing (triaxial testing, for example) may not be able to provide sufficient damage
evolution law and definition of damage strain may need to include some more subtle reference to the nature of the strain path
shearing with rotation of principal axes is likely to be especially damaging
feasible to introduce other evolution laws which relate change (increase or decrease) of scalar measure of structure r to chemical environment or time or temperature effects
Cam clay can be regained by setting r = 1, R = 1

## Slide 31
hierarchical extension of 'bubble' model to include effects of structure
other evolution laws: relate change (increase or decrease) of scalar measure of structure r to chemical environment or time or temperature effects
Cam clay can be regained by setting r = 1, R = 1

## Slide 32
Norrköping clay – calibration tests
Rouainia & Muir Wood (2000)

## Slide 33
Norrköping clay – parametric variation
Rouainia & Muir Wood (2000)

## Slide 34
Norrköping clay – undrained – isotropic consolidation
Rouainia & Muir Wood (2000)

## Slide 35
Norrköping clay – undrained – anisotropic consolidation
Rouainia & Muir Wood (2000)

## Slide 36
Norrköping clay – undrained – isotropic overconsolidation
Rouainia & Muir Wood (2000)

## Slide 37
simulation experiment
Bothkennar clay
results normalised by Hvorslev equivalent consolidation pressure p'e for structureless soil
Gajo & Muir Wood, 2001

## Slide 38
Hierarchical extensions of Cam clay
it is relatively straightforward to add extra features to a soil model
advantage in using well known model as basis – check implementation – acceptability
extra features imply additional soil parameters and additional calibration tests
seek adequate complexity in modelling – match complexity of model to availability of data and needs of application